## Slide 1
Path Planning – Driving Requirements
Level 1 | Level 2 | Level 3 | 
The system shall perform a search for targets. | The system shall navigate an unknown environment, using partial, prior information, e.g. building plans. | 1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles
 |  | 1.2.2 | The system shall plan vehicle trajectories through the environment
 |  | 1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present.
 |  | 1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles.
Level 1 | Level 2 | Level 3 | 
The system shall be autonomous, i.e. no human input once the system begins a search. | The system shall not have external navigation and targeting commands | 4.4.1 | The system shall make all navigation decisions onboard.

## Slide 2: 2 Steps
Path Planning – High Level
Step 1:
Waypoint Generation
  Develop list of nodes within operating space
  Exclude obstacles from list
Step 2:
Path determination
  Select nodes which:
    Lead from start -> goal
    Inherently avoid obstacles due to step 1

## Slide 3
Path Planning – Proposed Solution
Voronoi path generation
  Generates nodes which are equidistant from obstacles
A* search
  Least cost node selection
  Cost = g(n) + h(n)
    g(n) = known cost (previously traversed)
    h(n) = estimate of node -> goal distance

## Slide 4
Path Planning - Methodology
Voronoi Node Generation
Inputs
Array of X and Y values that represent obstacles
Process
Outputs
Ordered list of polygon vertices representing points equidistant from obstacles

## Slide 5
Path Planning – Methodology (Voronoi)
Fewer nodes to evaluate than probabilistic methods
Optimum obstacle margin
  Paths automatically as far from obstacles as possible
Open spaces are often node sparse
  Depending on size of room, could require node addition to fill out space

## Slide 6
Path Planning – Voronoi Performance
Processing time is more or less linear
Note that our space is define in 340 (red *)

## Slide 7
Path Planning - Methodology
A*
Inputs
Array of X and Y values that represent waypoint possibilities
Process
Determine path based on least cost approach
Cost = g(n) + h(n)
  g(n) = known cost (previously traversed)
  h(n) = estimate of node -> goal distance
Outputs
Array of nodes defining path

## Slide 8
Path Planning – Summary
Level 3 |  | PRM/NN+2Opt Solution
1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles | - Nodes are randomly placed in open space. - Collision-prone node connections are discarded.
1.2.2 | The system shall plan vehicle trajectories through the environment | - Roadmap provides collision-free paths to most points in open space. - NN+2Opt method provides a trajectory to visit most of the open space on the roadmap.
1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present. | - NN+2Opt provides a trajectory plan that avoids obstacles and visits most of the open space on the roadmap.
1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles | - PRM has the capability to configure the minimum distance from obstacles.
4.4.1 | The system shall make all navigation decisions onboard. | - PRM approach provides position set points in open space with collision-free paths between them.

## Slide 9
Path Planning – Backup Slides

## Slide 10
FlyNet: Autonomous Quadcopter Search and Rescue