## Slide 1
FlyNet: Planning
Requirements Motivation

## Slide 2
FlyNet: Planning
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space

## Slide 3
FlyNet: Planning
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space
Update plan based on dynamic environment
“Roadblock”
“Target”
“Complete Block”

## Slide 4
FlyNet: Planning
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space
Update plan based on dynamic environment
“Roadblock”
“Target”
“Complete Block”

## Slide 5
FlyNet: Planning
Plath Planning Alternatives
Cell Decomposition
  Break the map down into a grid
  Determine valid connections in the grid space
  Easy/fast to compute
  Cannot capture complex vehicle dynamics
Potential Fields
  Generate potential fields for plan
  Attract to desired trajectory
  Repel from obstacles
  Easy/fast to compute
  Struggles with local minima (ie rooms)
Sampling based methods
  Sample potential robot states randomly
  Connect states by checking for collisions and dynamics feasibility
  Captures high-dimensional robot states
  Captures complex problem constraints
See: http://ompl.kavrakilab.org/OMPL_Primer.pdf

## Slide 6
FlyNet: Planning
Plath Planning Alternatives
Cell Decomposition
  Break the map down into a grid
  Determine valid connections in the grid space
  Easy/fast to compute
  Cannot capture complex vehicle dynamics
Potential Fields
  Generate potential fields for plan
  Attract to desired trajectory
  Repel from obstacles
  Easy/fast to compute
  Struggles with local minima (ie rooms)
Sampling based methods
  Sample potential robot states randomly
  Connect states by checking for collisions and dynamics feasibility
  Captures high-dimensional robot states
  Captures complex problem constraints
See: http://ompl.kavrakilab.org/OMPL_Primer.pdf

## Slide 7
FlyNet: Planning
From: http://ompl.kavrakilab.org/OMPL_Primer.pdf
Plath Planning Alternatives
Probabilistic Roadmap
  Randomly sample robotic states over the entire space
  Connect states using collision detection and dynamics verification
  Use this map to plan movements through space
  Query this roadmap for new goals
  Need to re-plan roadmap if environment changes

## Slide 8
FlyNet: Planning
From: http://ompl.kavrakilab.org/OMPL_Primer.pdf
Plath Planning Alternatives
Tree-Based Planners
  Seed a tree at the origin
  Randomly sample states near the current location
  Connect to all valid states based on collision detection and dynamics
  Grow this tree until we get to the goal
  Generates a single path from start to goal
  Need to grow a new tree for re-planning

## Slide 9
FlyNet: Planning
From: http://ompl.kavrakilab.org/OMPL_Primer.pdf
Plath Planning Alternatives
Tree-Based Planners
  Seed a tree at the origin
  Randomly sample states near the current location
  Connect to all valid states based on collision detection and dynamics
  Grow this tree until we get to the goal
  Generates a single path from start to goal
  Need to grow a new tree for re-planning

## Slide 10
FlyNet: Planning
The Open Motion Planning Library
Open-source library with implementations of sample-based planning algorithms
Provides plug-ins to ROS or standalone c++
Supports basic modeling of quad rotors moving in 3D Environment
  Uses point-mass model of quad with thrust and angular acceleration as controls
  Environment is defined by CAD model
Initial path planning conducted for built-in environment using RRT
Goal
Start
Trajectory
Top-Down View

## Slide 11
FlyNet: Planning
The Open Motion Planning Library
Supports benchmarking of planners
So far, 3D planners seem to take significant amounts of time:
40 seconds for an empty space!

## Slide 12
FlyNet: Planning
Path Planning Issues
Path planning can generate a near optimal trajectory for getting between a start position and goal
Ability to plan with well known map can generate trajectories free of obstacles in highly complex environment
  Require minimal human input
3D path planning can be time consuming

## Slide 13
FlyNet: Planning
Path Planning Issues
Path planning can generate a near optimal trajectory for getting between a start position and goal <- We need to make the goals
Ability to plan with well known map can generate trajectories free of obstacles in highly complex environment <- Our environments contain uncertainties
  Require minimal human input
3D path planning can be time consuming <- We will likely need to re-plan frequently

## Slide 14
FlyNet: Planning
Block Diagram (In Development)
Offline Planner
POS Set-Point: NED
Attitude Set-Point: Ɵɸɣ
A-priori MAP (CAD)
Trajectory Memory
Re-Plan
Updated Map from SLAM
<
Obstacle Distance from Guidance
Target Localization
Command Mux
Target location estimate:
Local NED
Local NED from SLAM
Feature Detection
Feature Mode
Mode Select

## Slide 15
FlyNet: Planning
Path Forward
Determine method for generating goal points
  Base this on search coverage by projecting FLiR FoV
Explore options for 2D planning
  Faster re-planning
Improve quadrotor model in OMPL
  Give roll/pitch limits
  Potentially eliminate orientation as a state for exploration
Benchmark various planning options in OMPL
Generate 3D or 2D model of our test space