## Slide 1
Path Planning – Driving Requirements
Level 1 | Level 2 | Level 3 | 
The system shall perform a search for targets. | The system shall navigate an unknown environment, using partial, prior information, e.g. building plans. | 1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles
 |  | 1.2.2 | The system shall plan vehicle trajectories through the environment
 |  | 1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present.
 |  | 1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles.
Level 1 | Level 2 | Level 3 | 
The system shall be autonomous, i.e. no human input once the system begins a search. | The system shall not have external navigation and targeting commands | 4.4.1 | The system shall make all navigation decisions onboard.

## Slide 2: 2 Steps
Path Planning – High Level
Step 1:
Roadmap Algorithm
  Develop list of nodes within operating space
  Exclude obstacles from list
Step 2:
Path Selection Algorithm
  Select nodes which:
    Lead from start -> goal
    Inherently avoid obstacles due to step 1

## Slide 3
Path Planning – Methodology (PRM)
Probabilistic Roadmap (PRM)
Inputs
Map grid with obstacles marked
Desired number of nodes
Desired maximum neighbor node distance
Process
Samples possible collision-free quadcopter configurations at random
Connect all nodes within the configured maximum neighbor distance
Discard any routes that intersect with obstacles
Outputs
Roadmap containing collision free nodes and edges representing possible vehicle configurations
Coverage across entirety of open space possible if number of nodes is sufficiently high

## Slide 4
Path Planning – Methodology (NN+2Opt)
Nearest Neighbor + 2-Opt
Inputs
Auto-generated goal coordinates (a set of uniformly distributed points in free space)
PRM
Process
Build cost-weighted adjacency matrix for each goal coordinate
Compute path to the nearest goal for each goal
Optimize path using 2-Opt which removes unnecessary path crossover
Outputs
Position set points that efficiently traverse all goal coordinates.
Image courtesy of https://en.wikipedia.org/wiki/2-opt
2-Opt Example
Nearest Neighbors

## Slide 5
Path Planning - Methodology
Voronoi Node Generation
Inputs
Array of X and Y values that represent obstacles
Process
Delaunay triangulation
  Draw circles through triangles node (obstacles)
  Connect centers of circles with lines
Outputs
Ordered list of polygon vertices representing points equidistant from obstacles

## Slide 6
Path Planning - Methodology
A*
Inputs
Array of X and Y values that represent waypoint possibilities
Process
Determine path based on least cost approach
Cost = g(n) + h(n)
  g(n) = known cost (previously traversed)
  h(n) = estimate of node -> goal distance
Outputs
Array of nodes defining path

## Slide 7
Path Planning – PRM Performance
Note: Performance based on Matlab computations
Processing time increases quadratically as the number of sampled configurations (nodes) increases
Increasing the number of nodes has diminishing returns for space coverage

## Slide 8
Path Planning – Voronoi Performance
Processing time is more or less linear
Note that our space is define in 340 (red *)

## Slide 9
Path Planning – Summary
Level 3 |  | Solution
1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles | - PRM: Nodes are randomly placed in open space. - Voronoi: Nodes selected based on distance from obstacles - Collision-prone node connections are discarded.
1.2.2 | The system shall plan vehicle trajectories through the environment | - Roadmap provides collision-free paths to most points in open space. - NN+2Opt/A* method provides a trajectory to visit most of the open space on the roadmap.
1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles | - PRM/Voronoi have the capability to configure the minimum distance from obstacles.
4.4.1 | The system shall make all navigation decisions onboard. | - PRM/Voronoi both provide position set points in open space with collision-free paths between them.

## Slide 10
Path Planning – Backup Slides
Notes: Incomplete Matlab algorithmic demonstration

## Slide 11
Path Planning – Backup PRM/NN-2opt
Probabilistic Roadmap (PRM)
  Creates roadmap based on randomly sampled quadcopter configurations in open space.
Nearest Neighbor (NN) with 2-Opt
  NN: Traverses roadmap goals by minimizing the total distance traveled from one node to the next.
  2-Opt: Optimizes path takes a route that crosses over itself and reorders it so it does not.

## Slide 12
Path Planning – Backup(PRM)
Probabilistically complete
  Chance to find route increases as number of nodes increases
Flexible and robust
  Collision avoidance threshold distance is configurable
  Number of sample nodes is configurable
  Maximum node neighbor distance configurable
  Re-plan only depends on updated map grid
Certain geometries where straight line connections cannot be made are difficult to navigate

## Slide 13
Path Planning – Backup (NN+2Opt)
Able to handle multiple goals
  The computational effort increases as the number of goals (i.e. rooms) increases
Total area coverage is configurable
  Depends on the granularity of auto-generated goal points
  Goal points can be recalculated during the mission

## Slide 14
Path Planning – Backup Voronoi/A*
Voronoi path generation
  Generates nodes which are equidistant from obstacles
A* search
  Least cost node selection
  Cost = g(n) + h(n)
    g(n) = known cost (previously traversed)
    h(n) = estimate of node -> goal distance

## Slide 15
Path Planning – Backup (Voronoi)
Fewer nodes to evaluate than probabilistic methods
Optimum obstacle margin
  Paths automatically as far from obstacles as possible
Open spaces are often node sparse
  Depending on size of room, could require node addition to fill out space

## Slide 16
Path Planning – NN+2Opt Performance
Note: Performance based on Matlab computations
Chart: Processing Time vs Number of Goals
| 1 | 4 | 7 | 6 | 6 | 10 | 14 | 14 | 14 | 10 | 6 | 7 | 1 | 4 | 4
Y-Values | 0.166 | 0.4434 | 1.1373 | 0.7026 | 0.6062 | 3.2837 | 5.9043 | 5.746 | 6.1816 | 3.125 | 0.48767 | 1.1477 | 0.010258 | 0.15137 | 0.33065
Processing time increases quadratically as the number of goals increases
Goals are auto-generated for uniform coverage of the open space

## Slide 17
FlyNet: Autonomous Quadcopter Search and Rescue