## Slide 1
ROS VRPN
Guidance Node
RTAB Map
MAVROS
Planning Node
Coord. Sys. Transform
Pose  Odom.
Pixhawk
Guidance
Quadrotor
Visual Odometry
(vx, vy, vz)
Depth and Grayscale Images
Ultrasound
(range x 5)
Obstacle Distance
(fused range x 5)
IMU
(ax-body,ay-body,az-body, p, q, r)
Vicon Pose
(xvic, yvic, zvic, ψset)
Vicon Pose in MAVROS C.S.
(xmap, ymap, zmap)
SLAM Pose
(xmap, ymap, zmap)
Setpoint Position/Attitude
(xset, yset, zset ϕset, θset, ψset)
Pixhawk Pose Estimate
(x, y, z, ϕ, θ, ψ)
Fused Odometry
(vx, vy, vz)
OctoMap
OctoMap  2D Map
2D Occupancy Grid
Motor PWM
Dynamics
Position Setpoint
Fused Pose Data
Main Node
Converter Node
Hardware
ROS Topic
Legend

## Slide 2
Pixhawk
Guidance
Motors
14.8 V
Battery (14.8V)
ESC
ODROID
FLiR
Radio Receiver
Power Distribution
5V
Regulator
14.8 V
14.8 V
5 V
5 V
5 V
5 V
WiFi Dongle
5 V

## Slide 3
Pixhawk
Guidance
ESC
ODROID
FLiR
Radio Receiver
SPI (Video)
USB
WiFi Dongle
I2C (Control)
PWM
USB
USB

## Slide 4
Pixhawk with PX4 Firmware
Aliencopter Bee Quadrotor
ODROID XU4
USB Hub
FLiR Sensor
FrSKY TFR4 Radio Receiver
Battery
Power Distribution Board
ESC/ Motor
Power Module
BEC
DJI Guidance
WiFi Adapter

## Slide 5: Final Architecture
Ground Station
ROS master
Communicates with onboard flight computer
Data visualization with RVIZ
Odroid XU4
Ubuntu 14.04
Runs RTAB Map
Runs planning algorithms
Runs target ID algorithms
DJI Guidance
Provides depth map, grayscale images, and visual odometry for RTAB Map
ROS publisher 10Hz
(HW Limited)
SSH via WiFi
ROS
Pixhawk Autopilot
Running PX4 Firmware
Accept position/attitude setpoints from planning algorithm
Runs onboard position controllers
Provides attitude information to target ID algorithms
FLiR Sensor
Provides IR images for human identification
UART Cable