## Slide 1: Final Architecture
Ground Station
ROS master
Communicates with onboard flight computer
Data visualization with RVIZ
Runs laser scanmatcher
Odroid U3
Ubuntu 14.04
Runs Kalman Filter
Runs AMCL
Runs Flight Controllers
PX4Flow
Measures Altitude
Hokuyo Laser scanner
Measurements used by AMCL for position and scanmatcher for velocity
Pixhawk Autopilot
Running Arducopter Firmware
Providing accelerometer measurements and Euler angles to KF
Providing attitude control (stabilize mode)
3DR X8, X8+
Octo-Quad configuration
~15 min flight time with 10000mA 4S battery
ROS publisher 40Hz (HW Limited)
ROS publisher 10Hz
(HW Limited)
SSH via WiFi
ROS
PyMavlink
20Hz
(SW Limited)
Motor ESCs

## Slide 2: ROS Architecture
Software Node
Key
Topic
Hardware Node
Pre-loaded Info
Localization
Path Planner
NAV
PWM Conv
Scan Matcher
PX4 Flow
Hokuyo
PixHawk
Map
Notes: Quinn
Update PixHawk outputs
Break localization into Kalman Filter and Particle Filter
Change odom to be rates

## Slide 3: Hardware Configuration
Intro
Overview
Design
Battery
Power Distribution Board
ublox LEA-6H GPS+MAG
FrSKY TFR4 Radio Receiver
USB Hub
ESC/ Motor
Power Module
O-Droid U3
PX4Flow
BEC
Sony Camera
Pixhawk with APM Arducopter Firmware
Hokuyo URG-04LX-UG01 Laser Scanner
To USB Hub
Wrap Up