## Slide 1
FlyNet: Autonomous Quadcopter Search and Rescue

## Slide 2: Vehicle Control
FlyNet: Autonomous Quadcopter Search and Rescue
Strategy:
Use as many onboard(autopilot) processes as possible
Use off the shelf hardware/software wherever possible
1st Iteration:
Run position/attitude/altitude controllers on Pixhawk
Use Pixhawk controllers

## Slide 3: Pixhawk Hardware
FlyNet: Autonomous Quadcopter Search and Rescue
Notes: Replace gps with local ned

## Slide 4
FlyNet: Autonomous Quadcopter Search and Rescue

## Slide 5
FlyNet: Autonomous Quadcopter Search and Rescue
Path Planner
Controller Decision Gate
Position
Acceleration
Velocity
Quadrotor
IMU
p,q,r | ax-b ay-b az-b |φbθbψb
Altitude

## Slide 6: Pixhawk – Off-board Computer Interface
FlyNet: Autonomous Quadcopter Search and Rescue
uORB publish/subcribe bus
Actuator & Sensor Interface
Safety Controller
Local NED Subscriber
Position Controller
Attitude Controller
Planner Generated Set point
ROS publish/subscribe bus
SLAM
Obstacle Avoidance
Local NED Publisher
Path
Planner
UART MAVlink
>250 Hz
< 1 ms latency
Embedded Controller (Pixhawk)
Linux Companion Computer
Custom
Modified
Preexisting