## Slide 1
FlyNet: Mid Semester Review
October 21st, 2015
Critical Design Review

## Slide 2
Overview
Project Overview
  Organizational Chart
  Concept of Operations
  System Overview
Subsystem Overviews
  Hardware Platform
  Flight Controls / Autopilot Interfacing
  Perception and Mapping
  Target Identification
  Planning and Guidance
End of semester demo
Deliverables
Requirement Updates
Budget
Schedule

## Slide 3
Organization Chart

## Slide 4
Organization Chart

## Slide 5
Concept of Operations
“Roadblock”
“Target”
Entry/Exit Point
“Complete Block”
Autonomously explore an indoor environment with a team of ground/air robots in a disaster area situation
Map the environment and communicate that map to first responders
Identify humans in the environment and report their locations to first responders
Deliver a package to humans in the environment

## Slide 6
FlyNet: System Block Diagram
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
= Internal Software hosted on XU4
= Off board system
= Sensor
= Pixhawk
= Internal software connection using ROS publish/subscribe
= USB connection
= Wireless link
= SPI Video

## Slide 7
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To SLAM:
5 x Grey-Scale Image @ 20 Hz
2 x Depth Map @ 20 Hz
Body Frame Velocity
(vN,vE,vD) @ 10 Hz
To Planning:
5 x Obstacle distance @ 20 Hz
FlyNet: System Block Diagram

## Slide 8
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Target D and T:
80x60 IR images @ 8.6 Hz
FlyNet: System Block Diagram

## Slide 9
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Planning:
Map (in octo-map representation) @ ~10 Hz
To Planning and Flight Control:
Local NED @ ~10 Hz
To Target D and T:
Local NED @ ~10 Hz
Depth Map @ ~20 Hz
From Guidance:
See Guidance Slide
From Target D and T:
Target position estimate in local NED @ <8.6 Hz
FlyNet: System Block Diagram

## Slide 10
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Planning, SLAM, Ground Station:
Target position estimate in local NED @ <8.6 Hz
From SLAM:
Local NED estimate @ ~10 Hz
Depth Map @ ~20 Hz
From Flight Control:
Attitude estimate in Euler Angles @ TBD Hz
From FLiR:
80x60 IR images @ 8.6 Hz
FlyNet: System Block Diagram

## Slide 11
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Flight Control:
POS Command in Local (or Global) NED @ Variable Hz
Attitude Command in Euler Angles @ Variable Hz
From SLAM:
Local NED estimate @ ~10 Hz, Map @ ~10 Hz
From Guidance:
5 x Obstacle distance @ 20 Hz
From Target D and T:
Target Location Estimate @ <8.6 Hz
From Ground Station:
Operator Override Commands
FlyNet: System Block Diagram

## Slide 12
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Target D and T:
Attitude estimate in Euler Angles @ TBD Hz
From SLAM:
Local NED estimate @ ~10 Hz, Map @ ~10 Hz
From Guidance (TBD):
1 x Sonar distance @ 20 Hz
From Planning:
Set-points (see planning slide)
From RC Overrides:
Arm signal
Max throttle control
FlyNet: System Block Diagram

## Slide 13
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
FlyNet: System Block Diagram

## Slide 14
Autonomous Quadcopter Flight Control
Level 1 | Level 2 | Level 3 | 
The system shall perform a search for targets. | The system shall navigate an unknown environment, using partial, prior information, e.g. building plans. | 1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles
 |  | 1.2.2 | The system shall plan vehicle trajectories through the environment
 |  | 1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present.
 |  | 1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles.
 | The system shall search a 50,000 ft2 area | 1.3.1 | The system shall have power to sustain 10 minutes of search time with full payload
 |  | 1.3.2 | The system shall travel a minimum of 1 mile

## Slide 15
Hardware Solution
ODROID XU4
Pixhawk with PX4 Firmware
ODROID XU4 acts as onboard supervisory computer
Interfaces with planning and perception subsystems to feed set points to the autopilot
Pixhawk autopilot will be used to control the vehicle
Pixhawk was available, cheap enough to procure for multiple platforms, supports open source firmware for flexible software development, and legacy code and experience existed in house
Pixhawk supports position, velocity, or attitude set points for flexible interfacing options
Pixhawk supports the use of external vision position estimate solutions, such as the one provided from SLAM

## Slide 16
Software Solution
Robotic operating system was used to integrate the perception, planning, and flight control subsystems
ROS abstracts messaging layers, manages dependencies, is open source, supports heterogeneous code, and has existing code base to support each of the required subsystems
Built on a publish/subscriber and service/consumer architecture
Software is developed as interconnected nodes accomplishing various tasks
The flight control software was architected to maximize code reusability and modularity
  Focus on standardizing interfaces
  Support swapping nodes as new subsystem functionality becomes mature
  Support future integration with software-in-the-loop simulations

## Slide 17
ROS Architecture
Local Position Estimate
Coordinate Frame Translation
Trajectory Generation
Core Flight Control Nodes

## Slide 18
ROS Architecture
Perception Subsystem
Planning
Subsystem
Core Flight Control Nodes

## Slide 19
Control and Dynamics Modeling
Assumptions placeholder

## Slide 20
Control and Dynamics Modeling

## Slide 21
Control and Dynamics Modeling

## Slide 22
Results

## Slide 23
Results

## Slide 24
Results

## Slide 25
Path Forward
Tune control gains based on modeling results
Refine dynamics model from flight data
Integrate subsystems as they reach maturity
Integrate obstacle avoidance functionality in the ROS architecture
Develop software to overcome obstacles using altitude diversity
Utilize SITL simulations to verify flight control software functionality before hardware deployment

## Slide 26
Budget
Currently Spent:
  $1855.00 / 12.4%
Previous spending:
  Quadrotor platform
  Several single board computers (ODROID XU4)
Planned Spending:
  Secondary platform:
    Estimated to be $3000 per platform