## Slide 1
Target Identification and Tracking - Motivation
Level 1 | Level 2 | Level 3 | 
The system shall perform a search for targets. | The system shall visually identify targets | 1.1.1 | The system shall have visual sensor(s)
 |  | 1.1.2 | The system shall be capable of processing imagery
 |  | 1.1.3 | The system shall locate individual targets with 95% probability of detection
 |  | 1.1.4 | The system shall identify human targets within 5 meters
Level 1 | Level 2 | Level 3 | 
The system shall track visually identified targets | Each PPU shall have the ability to track targets | 2.1.1 | The PPU shall estimate the target position to within 0.5 meters
 |  | 2.1.2 | Each PPU shall estimate at least 2 visually identified targets
 |  | 2.1.3 | Each PPU shall maintain estimates of all confirmed target tracks
 | PPUs shall track targets moving up to 2 m/s along the ground | 2.2.1 | PPUs shall process target estimates at 10 Hz

## Slide 2
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker

## Slide 3
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Performance varies greatly with lighting conditions.
Increased complexity

## Slide 4
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Provides great contrast between human target and background
Simplifies target identification problem
Not sensitive to lighting conditions

## Slide 5
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Depth may be provided by SLAM sensors

## Slide 6
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Time ordered history of position of target is not required
No need to discriminate between multiple targets.

## Slide 7
Target Identification and Tracking
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker

## Slide 8
Target Identification and Tracking
Design Solution: FLiR Lepton LWIR Camera with Image Masking and Contour Tracking
FLiR Lepton on Breakout Board
FLiR Lepton on Quarter for Scale

## Slide 9
Target Identification and Tracking
Design Solution: FLiR Lepton LWIR Camera with Image Masking and Contour Tracking
Specifications:
  LWIR sensor: 8-14 μm
  51-deg HFOV, 63.5-deg diagonal FOV
  80 x 60 pixels
  Thermal sensitivity <50 mK
  MIPI and SPI video interfaces
  I2C control interface
  Power draw <160 mW
  8.6 Hz frame rate
  Mass 0.55 g

## Slide 10
Target Identification and Tracking
Tracking Algorithm Overview

## Slide 11
Target Identification and Tracking
Tracking Algorithm Overview
Masking +
Morphology

## Slide 12
Target Identification and Tracking
Tracking Algorithm Overview
Contour Detection
And Selection

## Slide 13
Target Identification and Tracking
Algorithm Performance
Matlab was used to generate simulate FLiR LWIR images and Guidance depth map images
These images were processed to determine sensitivity to noise and target position
Simulated 80x60 FLiR Image
Simulated 320x240 Guidance
Depth Map
Simulated Human-Sized Target at 5m

## Slide 14
Target Identification and Tracking
Algorithm Performance
Error due to noise in Guidance depth map was on the order of the noise itself
Error due to position in frame is negligible
Simulated 80x60 FLiR Image
Simulated 320x240 Guidance
Depth Map
Simulated Human-Sized Target at 5m

## Slide 15
Target Identification and Tracking
Tracking - ROS Integration

## Slide 16
Target Identification and Tracking
FLiR - Odroid Integration

## Slide 17
Target Identification and Tracking - Motivation
Level 3 |  | How is Requirement Satisfied
1.1.1 | The system shall have visual sensor(s) | FLiR Lepton LWIR Camera
1.1.2 | The system shall be capable of processing imagery | OpenCV
1.1.3 | The system shall locate individual targets with 95% probability of detection | Use of LWIR instead of visual
1.1.4 | The system shall identify human targets within 5 meters | Sufficient resolution to detect humans at 5 m
Level 3 |  | How is Requirement Satisfied
2.1.1 | The PPU shall estimate the target position to within 0.5 meters | As long as depth map is accurate enough, this is not a problem
2.1.2 | Each PPU shall estimate at least 2 visually identified targets | Number of tracked targets is configurable
2.1.3 | Each PPU shall maintain estimates of all confirmed target tracks | Estimates are published to ROS nodes
2.2.1 | PPUs shall process target estimates at 10 Hz | Small images and simple algorithm = very fast processing (Close to real time with HD images)