## Slide 1
Critical Design Review
December 9th, 2015
F l y N e t
Drew Ellison
Austin Anderson
Bryce Hill
Steve McGuire
Prashant Ganesh
Ed Meletyan
Tyler Clayton
Matt Busby
Taylor Dean

## Slide 2
Team Organization
Concept of Operations
System Design Overview
Subsystem Overviews:
  Hardware
  Planning
  Flight Controls
  Perception
    SLAM
    Target Identification
Presentation Overview

## Slide 3
Organizational Chart
Drew Ellison
Project Manager
Steve McGuire
PerceptionLead
Bryce Hill
PlanningLead
Ed Meletyan
Simulation Lead
Austin Anderson
Systems Engineer
Taylor Dean
Perception Team
Tyler Clayton
Hardware Lead
Matt Busby
Test Lead
Prashant Ganesh
Hardware Team

## Slide 4
“Roadblock”
“Target”
Entry/Exit Point
“Complete Block”
Autonomously explore an indoor environment with a team of ground/air robots in a disaster area situation
Map the environment and communicate that map to first responders
Identify humans in the environment and report their locations to first responders
Deliver a package to humans in the environment
Presentation Overview

## Slide 5
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
= Internal Software hosted on XU4
= Off board system
= Sensor
= Pixhawk
= Internal software connection using ROS publish/subscribe
= USB connection
= Wireless link
= SPI Video
Presentation Overview

## Slide 6
Guidance Node
RTAB Map
MAVROS
Planning Nodes
Pose  Odom.
Pixhawk
Quadrotor
Visual Odometry
(vx, vy, vz)
Grayscale Images
Obstacle Distance
(fused range x 5)
SLAM Pose
(xmap, ymap, zmap)
Setpoint Position/Attitude
(xset, yset, zset ϕset, θset, ψset)
Pixhawk Pose Estimate
(x, y, z, ϕ, θ, ψ)
Fused Odometry
(vx, vy, vz)
OctoMap
OctoMap  2D Map
2D Occupancy Grid
Motor PWM
Dynamics
Position Setpoint
Fused Pose Data
Main Node
Converter Node
Hardware
ROS Topic
Guidance
Presentation Overview

## Slide 7
Ultrasonics
Stereo Camera Pair
Holes for Custom Guidance Mount
Quad Structure

## Slide 8
Underside of quad with Guidance sensor mounting bars
(red)
Guidance Sensor attached to quadcopter
Quad Structure

## Slide 9
USB 2.0 (#1)
(Position
Commands)
Pixhawk with PX4 Firmware
ODROID XU4
FLiR Sensor
FrSKY TFR4 Radio Receiver
Battery (14.8V)
ESC/ Motor
DJI Guidance
WiFi Adapter
Comms
Power
SPI (video)
I2C (control)
USB 3.0 (#0)
USB 2.0 (#2)
(odometry & BW images)
UART
(RC inputs)
PWM Signals
Quad System Design

## Slide 10
Component | Qty | Mass (each) [g]
AlienCopter Bee Frame | 1 | 303.0
Custom Landing Gear | 4 | 22.5
Custom Propeller Guards | 2 | 123.0
ODROID XU4 (w/ case and Wi-Fi dongle) | 1 | 83.5
ODROID Expansion Shield | 1 | 21.1
DJI Guidance Sensor (w/ mounting hardware) | 1 | 470.4
Pixhawk | 1 | 40.3
FliR Lepton LWIR Camera | 1 | 0.6
FrSKY TFR4 Radio Receiver | 1 | 8.7
Power Distribution Board | 1 | 21.0
SunnySky V2216-12 II Motors | 4 | 68.7
10x4.7 Propellers | 4 | 11.1
20A ESC | 4 | 28.4
Turnigy Multistar 4S 10.0 LiPo Battery Pack | 1 | 815.8
 | Total | 2365.3
Mass Budget

## Slide 11
Pixhawk
Guidance
Motors
14.8 V , .81 A
Battery (14.8V)
ESC
ODROID
FLiR
Radio Receiver
Power Distribution
5V
Regulator
14.8 V , 2-20 A
14.8 V
5 V , 0.3 A
5 V , 4 A
WiFi Dongle
Power Distribution FBD

## Slide 12
Component | Qty | Nominal Voltage [V] | Current Draw [mA] | Power Consumption [mW]
ODROID XU4 (powers FLiR & Wi-Fi) | 1 | 5 | 4000 | 20000
DJI Guidance Sensor | 1 | 14.8 | 810 | 12000
Pixhawk (powers radio receiver) | 1 | 5 | 300 | 1500
SunnySky V2216-12 II Motors | 4 | 14.8 | 4730 | 70017
Total |  |  | 24030 | 313568
Motors use 89.3% of total power consumption (78.7% of Current Draw)
Motor estimated at hovering condition
Power Budget

## Slide 13
Mass [kg] | Time [min]
2.37 | 20
2.60 (0.5 lb) | 17.5
2.82 (1.0 lb) | 15.6
3.87 (MAX) | 10
Note, all data points shown above are theoretical
Flight Endurance

## Slide 14
Stopping Distance Simulation

## Slide 15
a | 4.72E-06
b | 8.50E-03
c | -1.947
Propeller | Throttle | Current Draw [A] | Thrust [g]
10x3.8 | 50% | 3.3 | 480
 | 65% | 5.4 | 650
 | 75% | 8.1 | 810
 | 85% | 11.9 | 1030
 | 100% | 15.2 | 1210
Experimental Results of SunnySky V2212 Motors
Experimental results were found for 10x3.8 propeller
Quadratic fit to get an equation for current depending on thrust
Motor Current Estimation

## Slide 16
Aluminum Bracket:
FLiR Sensor Mounting

## Slide 17
Nylon Stand-Offs
Mount Design

## Slide 18: Requirement Motivation
The system shall consist of a team of at least 2 robots
The system shall have at least 1 aerial vehicle
Proposed Solution
Use ground robots to perform the following function:
  Serve as a test bed for planning and perception algorithms
  Map in parallel to quad copter
Alternative Development Platform

## Slide 19
Proposed to use TurtleBot with:
  iRobot Create
  Guidance
  Odroid XU4
  Kinect Mounting Hardware
  Xtion Pro (optional)
  FLiR sensor
Ground Robot Description

## Slide 20
IMU and Wheel Odometry
Odroid XU4
WiFi
Adapter
Battery
Power Distribution Board
Motor
Power Module
Guidance
FLiR
Xtion
(optional)
Ground Robot Architecture

## Slide 21
Odroid XU 4
Ubuntu 14.04
Runs Hector_Slam algorithms
Runs path planning algorithms for the ground
Acts as a task allocator (incase of multiple quadcopters)
Ground Station
Communicates between the on-board computer
Aerial Robot
Current position
Location of target (if found)
Asus Xtion Pro (Optional)
Provides depth map, grayscale images, and visual odometry for RTAB Map
USB 3.0
WiFi
WiFi
FLiR
Provides IR images for human identification
Guidance
Provides depth map, grayscale images, and visual odometry for RTAB Map
Ground Robot Comm.

## Slide 22
Understanding the working of the current TurtleBot setup
Fabricate additional hardware to accommodate hardware additions
Implement path planning and perception algorithms
Integrate with aerial robot
Ground Robot Path Forward

## Slide 23
Path Planning
Level 3 | Solution
The vehicles shall avoid unrecoverable collisions with obstacles | - PRM: Nodes are randomly placed in open space. - Voronoi: Nodes selected based on distance from obstacles - Collision-prone node connections are discarded.
The system shall plan vehicle trajectories through the environment | - Roadmap provides collision-free paths to most points in open space. - NN+2Opt/A* method provides a trajectory to visit most of the open space on the roadmap.
The aerial vehicle will maintain a minimum distance of 5 cm from obstacles | - PRM/Voronoi have the capability to configure the minimum distance from obstacles.
The system shall make all navigation decisions onboard. | - PRM/Voronoi both provide position set points in open space with collision-free paths between them.

## Slide 24: 2 Steps
Step 1:
Roadmap Algorithm
  Develop list of nodes within operating space
  Exclude obstacles from list
Step 2:
Path Selection Algorithm
  Select nodes which:
    Lead from start -> goal
    Inherently avoid obstacles due to step 1
  Coverage of the entire space
Path Planning Solution
Notes: 2 options for both

## Slide 25
Probabilistic Roadmap (PRM)
Inputs
Map grid with obstacles marked
Desired number of nodes
Desired maximum neighbor node distance
Process
Samples possible collision-free quadcopter configurations at random
Connect all nodes within the configured maximum neighbor distance
Discard any routes that intersect with obstacles
Outputs
Roadmap containing collision free nodes and edges representing possible vehicle configurations
Coverage across entirety of open space possible if number of nodes is sufficiently high
Roadmap (PRM)

## Slide 26
Voronoi Node Generation
Inputs
Array of X and Y values that represent obstacles
Process
Delaunay triangulation
  Draw circles through triangles (where vertices are the obstacles)
  Connect centers of circles with lines
Outputs
Ordered list of polygon vertices representing points equidistant from obstacles
Roadmap (Voronoi)

## Slide 27
Voronoi Node Generation
Inputs
Array of X and Y values that represent obstacles
Process
Delaunay triangulation
  Draw circles through triangles (where vertices are the obstacles)
  Connect centers of circles with lines
Outputs
Ordered list of polygon vertices representing points equidistant from obstacles
Roadmap (Voronoi)

## Slide 28
Nearest Neighbor + 2-Opt
Inputs
Auto-generated goal coordinates (a set of uniformly distributed points in free space)
PRM
Process
Build cost-weighted adjacency matrix for each goal coordinate
Compute path to the nearest goal for each goal
Optimize path using 2-Opt which removes unnecessary path crossover
Outputs
Position set points that efficiently traverse all goal coordinates.
Image courtesy of https://en.wikipedia.org/wiki/2-opt
2-Opt Example
Nearest Neighbors
NN + 2 Opt
Notes: Advantage of 2opt?

## Slide 29
Able to handle multiple goals
  The computational effort increases as the number of goals (i.e. rooms) increases
Total area coverage is configurable
  Depends on the granularity of auto-generated goal points
  Goal points can be recalculated during the mission
NN + 2Opt

## Slide 30
Note: Performance based on Matlab computations
Processing time increases quadratically as the number of sampled configurations (nodes) increases
Increasing the number of nodes has diminishing returns for space coverage
PRM Performance

## Slide 31
Processing time is more or less linear
Note that our space is define in 340 (red *)
Voronoi Performance

## Slide 32
Level 3 | Solution
The vehicles shall avoid unrecoverable collisions with obstacles | Waypoints around obstacles through communication with Pixhawk
The system shall plan vehicle trajectories through the environment | Waypoint generator running on ODROID
The vehicles shall move through the environment along planned trajectories to within 20cm RMS error of the planned trajectory when no obstacles are present. | PX4 Position Control system onboard Pixhawk with waypoint generation on ODROID. Control gains must be modeled to meet this requirement
The aerial vehicle will maintain a minimum distance of 5 cm from obstacles. | Waypoint generation around obstacles with a quick update on PX4 waypoints when obstacles are within distance thresholds
The system shall have power to sustain 10 minutes of search time with full payload | The system must travel at ~1.5 m/s on average. PX4 controllers support this velocity and has been flown up to
The system shall search an area of 50,000 ft2 | 
Flight Controls (FC)

## Slide 33
ODROID XU4
Pixhawk with PX4 Firmware
ODROID XU4 acts as onboard supervisory computer
Interfaces with planning and perception subsystems to feed set points to the autopilot
Pixhawk autopilot will be used to control the vehicle
Pixhawk was available, cheap enough to procure for multiple platforms, supports open source firmware for flexible software development, and legacy code and experience existed in house
Pixhawk supports position, velocity, or attitude set points for flexible interfacing options
Pixhawk supports the use of external vision position estimate solutions, such as the one provided from SLAM
FC Hardware

## Slide 34
Robotic operating system was used to integrate the perception, planning, and flight control subsystems
ROS abstracts messaging layers, manages dependencies, is open source, supports heterogeneous code, and has existing code base to support each of the required subsystems
Built on a publish/subscriber and service/consumer architecture
Software is developed as interconnected nodes accomplishing various tasks
The flight control software was architected to maximize code reusability and modularity
  Focus on standardizing interfaces
  Support swapping nodes as new subsystem functionality becomes mature
  Support future integration with software-in-the-loop simulations
FC Software

## Slide 35
Local Position Estimate
Coordinate Frame Translation
Trajectory Generation
Core Flight Control Nodes
FC ROS Architecture

## Slide 36
Perception Subsystem
Planning
Subsystem
FC ROS Architecture
Core Flight Control Nodes

## Slide 37
6 DoF Model
First order model for motor dynamics
Ignores sensor dynamics
Path commands given as inertial x, y, z and yaw at time t
Model does not include:
  Airframe drag
  Blade flapping
  Wall and boundary effects
Control Dynamics Modeling

## Slide 38
Altitude Step Response
Lateral Step Response
Yaw Step Response
Control Dynamics Modeling

## Slide 39
Control Dynamics Modeling

## Slide 40
Flight Results

## Slide 41
Flight Data for Square Trajectory with Altitude Hold
Flight Results

## Slide 42
Flight Data for Yaw Step Command with Position hold
Flight Results

## Slide 43
Tune control gains based on modeling results
Refine dynamics model from flight data
Integrate subsystems as they reach maturity
Integrate obstacle avoidance functionality in the ROS architecture
Develop software to overcome obstacles using altitude diversity
Utilize SITL simulations to verify flight control software functionality before hardware deployment
FC Path Forward

## Slide 44
Level 3 | How is Requirement Satisfied | 
1.1.1 | The system shall have visual sensor(s) | Guidance cameras
1.1.2 | The system shall be capable of processing imagery | Guidance and software pipelines
1.2.1 | The system shall avoid unrecoverable collisions with obstacles | Obstacle detection via Guidance
1.2.2 | The system shall plan vehicle trajectories through the environment | Map production from RTABMap
Level 3 | How is Requirement Satisfied | 
2.1.1 | The PPU shall estimate target position to within 0.5 m | Software stereo pipeline's depth image coupled with RTABMap position estimate
4.1.2 | The system shall perform perception onboard | Guidance + RTABMap
Perception

## Slide 45
Major Design Choices:
  Custom vs Off-The-Shelf SLAM Package
  Underlying algorithmic options
    Sparse vs Dense
    Loop closure support
  Image processing choices:
    Onboard
    Auxiliary processor
  Image sensor choices:
    Monocular
    Visual + Depth
    Stereo pair
  Additional sensor options
    Ultrasound
    Scanning laser
    Laser altimeter
Design Choices

## Slide 46
Given timeline and team resources, development of a custom SLAM solution was not feasible
Turned to available software packages for their support of popular varieties of SLAM:
  RGBDSlam
  RTABMap
  CCNYSlam
  LSDSlam
Package determines sensors required and potential limitations
Loop closure determined to be a necessary feature to support operations in larger spaces
Necessary to have immediate position output for use in control system
Required to provide reasonable performance on a CPU that can be flown as payload
Custom vs. Prebuilt

## Slide 47
Design choice: RTABMap
Demonstrated capability aboard ARM SOCs
Provides for loop closure and map generation
Able to use a variety of sensor inputs (RGB-D / stereo / laser)
Uses sparse methods with a keyframe approach to minimize growth of map over large areas
SLAM Design Choice

## Slide 48
RTABMap requires an odometry source of some sort
  External odometry could offload a major source of CPU utilization
  Capable of generating odometry from monocular or stereo sensors
Design Choice: Guidance
Provides an external auxiliary processor to compute odometry, as well as sychronized global shutter stereo pairs
Includes ultrasound sensors as a bonus
Available as a turn-key solution
Onboard vs. Auxiliary

## Slide 49
Design choice: Stereo Pair
Depth maps produced by Guidance show poor performance, related to stereo pipeline algorithm parameters that can't be changed
Software stereo pipeline available to produce depth maps for use in target registration to 3D coordinates
RTABMap requires imagery input, either as a RGB-D or a stereo pair
Map produced by RGB+Depth
Map produced by stereo pair
Camera Choice

## Slide 50
Design choice: Laser altimeter
Guidance provides ultrasounds for coarse object detection and coarse altitude estimation
As testing proceeds, the laser altimeter may become necessary to ensure safe autonomous takeoffs and landings
Additional Sensors

## Slide 51
Guidance
RTAB Map
Additional Sensors

## Slide 52
Software Stereo Block Diagram

## Slide 53
Level 3 | How is Requirement Satisfied
The system shall have visual sensor(s) | FLiR Lepton LWIR Camera
The system shall be capable of processing imagery | OpenCV
The system shall locate individual targets with 95% probability of detection | Use of LWIR instead of visual
The system shall identify human targets within 5 meters | Sufficient resolution to detect humans at 5 m
Level 3 | How is Requirement Satisfied
The PPU shall estimate the target position to within 0.5 meters | As long as depth map is accurate enough, this is not a problem
Each PPU shall estimate at least 2 visually identified targets | Number of tracked targets is configurable
Each PPU shall maintain estimates of all confirmed target tracks | Estimates are published to ROS nodes
PPUs shall process target estimates at 10 Hz | Small images and simple algorithm = very fast processing (Close to real time with HD images)
Target ID and Tracking

## Slide 54
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Design Choices

## Slide 55
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Performance varies greatly with lighting conditions.
Increased complexity
Design Choices

## Slide 56
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Provides great contrast between human target and background
Simplifies target identification problem
Not sensitive to lighting conditions
Design Choices

## Slide 57
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Depth may be provided by SLAM sensors
Design Choices

## Slide 58
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Time ordered history of position of target is not required
No need to discriminate between multiple targets.
Design Choices

## Slide 59
Major Design Choices:
  Sensor Type
    Visual Spectrum Camera
    IR Spectrum Camera
    Stereo
    Monocular
  Tracking Algorithm
    Alternative Multiple Models
    Multiple Hypothesis Tracker
    Discrimination
    Simple Masking Tracker
Design Choices

## Slide 60
Design Solution: FLiR Lepton LWIR Camera with Image Masking and Contour Tracking
FLiR Lepton on Breakout Board
FLiR Lepton on Quarter for Scale
FLiR Sensor

## Slide 61
Design Solution: FLiR Lepton LWIR Camera with Image Masking and Contour Tracking
Specifications:
  LWIR sensor: 8-14 μm
  51-deg HFOV, 63.5-deg diagonal FOV
  80 x 60 pixels
  Thermal sensitivity <50 mK
  MIPI and SPI video interfaces
  I2C control interface
  Power draw <160 mW
  8.6 Hz frame rate
  Mass 0.55 g
FLiR Sensor

## Slide 62
Tracking Algorithm Overview

## Slide 63
Masking +
Morphology
Tracking Algorithm Overview

## Slide 64
Contour Detection
And Selection
Tracking Algorithm Overview

## Slide 65
Matlab was used to generate simulate FLiR LWIR images and Guidance depth map images
These images were processed to determine sensitivity to noise and target position
Simulated 80x60 FLiR Image
Simulated 320x240 Guidance
Depth Map
Simulated Human-Sized Target at 5m
Algorithm Performance

## Slide 66
Error due to noise in Guidance depth map was on the order of the noise itself
Error due to position in frame is negligible
Simulated 80x60 FLiR Image
Simulated 320x240 Guidance
Depth Map
Simulated Human-Sized Target at 5m
Algorithm Performance

## Slide 67
Stereo Depth Map Algorithm
ROS Integration

## Slide 68
Test Plan

## Slide 69
Test Plan
Notes: Fell behind schedule
Spent more time designing system then planned
  Designs changed
  Component issues
Talk about the most important test from this semester, and the two most important tests for next semester.

## Slide 70
Test Plan

## Slide 71
2 ft.
2 ft.
Hallway
Start with a known floor plan
Final Test Demo
Notes: Designed for this semester
Pushed back to next semester
Showcase functionality of the system
Performed in Fleming lab

## Slide 72
2 ft.
2 ft.
Hallway
Target
Start with a known floor plan
Target placed into area in unknown location
Final Test Demo

## Slide 73
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Start with a known floor plan
Target placed into area in unknown location
“Roadblocks” and a “Complete Block” added to simulate debris or obstacles
Final Test Demo

## Slide 74
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Entry/Exit Point
Start with a known floor plan
Target placed into area in unknown location
“Roadblocks” and a “Complete Block” added to simulate debris or obstacles
Also have a known entry/exit point
Final Test Demo

## Slide 75
System will autonomously fly and map entire space
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Entry/Exit Point
Guidance Sensor
SLAM Algorithm
Final Test Demo

## Slide 76
System will autonomously fly and map entire space
Planning subsystem will help avoid obstacles and recalculate trajectory
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Entry/Exit Point
Guidance Sensor
Obstacle Detection
Path Planning
!
Final Test Demo

## Slide 77
System will autonomously fly and map entire space
Planning subsystem will help avoid obstacles and recalculate trajectory
Target will be identified and located in the space
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Entry/Exit Point
Guidance Sensor
FLIR Camera & Target ID
Final Test Demo

## Slide 78
System will autonomously fly and map entire space
Planning subsystem will help avoid obstacles and recalculate trajectory
Target will be identified and located in the space
System will return to exit point to deliver map
2 ft.
2 ft.
Hallway
“Roadblock”
Target
“Complete Block”
Entry/Exit Point
Final Test Demo

## Slide 79
Building specs:
  4’ high walls made of 4’x8’ foam insulation paneling
  Walls held upright with wooden frames
  Doorframes will have extra reinforcements
  Wall design has been tested and proves to be viable
Final Test Demo

## Slide 80
Currently Spent:
  $3000.00 / 20.0%
Materials bought
  New quadrotor
  3 ODROID XU4s
  Demo materials
    Lumber, foam
  DJI Guidance
Budget

## Slide 81
Currently Spent:
  $1855.00 / 12.4%
Previous spending:
  Quadrotor platform
  Several single board computers (ODROID XU4)
Planned Spending:
  Secondary platform:
    Estimated to be $3000 per platform
Next Semester

## Slide 82
Thanks to Dr. Eric Frew, Joe Tanner, and Zohaib Mian for support and guidance

## Slide 83
http://wiki.ros.org/stereo_image_proc/Tutorials/ChoosingGoodStereoParameters
http://www.sekidorc.com/pdf/Guidance_UserManual_en_v1.2_150803.pdf
http://www.hobbyking.com/hobbyking/store/__61487__AlienCopter_Bee_full_Carbon_KIT_W_Clean_and_Dirty_System_and_PDB_W_BEC.html
http://www.hobbyking.com/hobbyking/store/__19626__FrSky_TFR4_4ch_2_4Ghz_Surface_Air_Receiver_FASST_Compatible.html
http://www.hardkernel.com/main/products/prdt_info.php
https://www.sparkfun.com/products/13233
https://developer.dji.com/guidance/
https://www.asus.com/3D-Sensor/Xtion_PRO/
https://store.3drobotics.com/products/3dr-pixhawk
References

## Slide 84
Questions?

## Slide 85
Backup
Notes: Incomplete Matlab algorithmic demonstration

## Slide 86
Probabilistic Roadmap (PRM)
  Creates roadmap based on randomly sampled quadcopter configurations in open space.
Nearest Neighbor (NN) with 2-Opt
  NN: Traverses roadmap goals by minimizing the total distance traveled from one node to the next.
  2-Opt: Optimizes path takes a route that crosses over itself and reorders it so it does not.
Backup

## Slide 87
Probabilistically complete
  Chance to find route increases as number of nodes increases
Flexible and robust
  Collision avoidance threshold distance is configurable
  Number of sample nodes is configurable
  Maximum node neighbor distance configurable
  Re-plan only depends on updated map grid
Certain geometries where straight line connections cannot be made are difficult to navigate
Backup

## Slide 88
Able to handle multiple goals
  The computational effort increases as the number of goals (i.e. rooms) increases
Total area coverage is configurable
  Depends on the granularity of auto-generated goal points
  Goal points can be recalculated during the mission
Backup

## Slide 89
Voronoi path generation
  Generates nodes which are equidistant from obstacles
A* search
  Least cost node selection
  Cost = g(n) + h(n)
    g(n) = known cost (previously traversed)
    h(n) = estimate of node -> goal distance
Backup

## Slide 90
Fewer nodes to evaluate than probabilistic methods
Optimum obstacle margin
  Paths automatically as far from obstacles as possible
Open spaces are often node sparse
  Depending on size of room, could require node addition to fill out space
Backup

## Slide 91
Note: Performance based on Matlab computations
Chart: Processing Time vs Number of Goals
| 1.0 | 4.0 | 7.0 | 6.0 | 6.0 | 10.0 | 14.0 | 14.0 | 14.0 | 10.0 | 6.0 | 7.0 | 1.0 | 4.0 | 4.0
Y-Values | 0.166 | 0.4434 | 1.1373 | 0.7026 | 0.6062 | 3.2837 | 5.9043 | 5.746 | 6.1816 | 3.125 | 0.48767 | 1.1477 | 0.010258 | 0.15137 | 0.33065
Processing time increases quadratically as the number of goals increases
Goals are auto-generated for uniform coverage of the open space
Backup

## Slide 92
FLiR - Odroid Integration
Backup