## Slide 1
FlyNet: Mid Semester Review
October 21st, 2015
Critical Design Review

## Slide 2
Overview
Organizational Chart
Concept of Operations
System Overview
Hardware Platform
Flight Controls / Autopilot Interfacing
Perception and Mapping
Target Identification
Planning and Guidance
End of semester demo
Deliverables
Requirement Updates
Budget
Schedule

## Slide 3
Organization Chart

## Slide 4
Organization Chart

## Slide 5
Concept of Operations
“Roadblock”
“Target”
Entry/Exit Point
“Complete Block”
Autonomously explore an indoor environment with a team of ground/air robots in a disaster area situation
Map the environment and communicate that map to first responders
Identify humans in the environment and report their locations to first responders
Deliver a package to humans in the environment

## Slide 6
FlyNet: System Block Diagram
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
= Internal Software hosted on Xu4
= Off board system
= Sensor
= Pixhawk
= Internal software connection using ROS publish/subscribe
= USB connection
= Wireless link
= SPI Video

## Slide 7
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To SLAM:
5 x Grey-Scale Image @ 20 Hz
2 x Depth Map @ 20 Hz
Body Frame Velocity
(vN,vE,vD) @ 10 Hz
To Planning:
5 x Obstacle distance @ 20 Hz
FlyNet: System Block Diagram

## Slide 8
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Target D and T:
80x60 IR images @ 8.6 Hz
FlyNet: System Block Diagram

## Slide 9
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Planning:
Map (in octo-map representation) @ ~10 Hz
To Planning and Flight Control:
Local NED @ ~10 Hz
To Target D and T:
Local NED @ ~10 Hz
Depth Map @ ~20 Hz
From Guidance:
See Guidance Slide
From Target D and T:
Target position estimate in local NED @ <8.6 Hz
FlyNet: System Block Diagram

## Slide 10
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Planning, SLAM, Ground Station:
Target position estimate in local NED @ <8.6 Hz
From SLAM:
Local NED estimate @ ~10 Hz
Depth Map @ ~20 Hz
From Flight Control:
Attitude estimate in Euler Angles @ TBD Hz
From FLiR:
80x60 IR images @ 8.6 Hz
FlyNet: System Block Diagram

## Slide 11
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Flight Control:
POS Command in Local (or Global) NED @ Variable Hz
Attitude Command in Euler Angles @ Variable Hz
From SLAM:
Local NED estimate @ ~10 Hz, Map @ ~10 Hz
From Guidance:
5 x Obstacle distance @ 20 Hz
From Target D and T:
Target Location Estimate @ <8.6 Hz
From Ground Station:
Operator Override Commands
FlyNet: System Block Diagram

## Slide 12
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
To Target D and T:
Attitude estimate in Euler Angles @ TBD Hz
From SLAM:
Local NED estimate @ ~10 Hz, Map @ ~10 Hz
From Guidance (TBD):
1 x Sonar distance @ 20 Hz
From Planning:
Set-points (see planning slide)
From RC Overrides:
Arm signal
Max throttle control
FlyNet: System Block Diagram

## Slide 13
Flight Control
SLAM
Planning
Target Detection and Tracking
Guidance
FLiR
RC Overrides
Ground Station
FlyNet: System Block Diagram

## Slide 14
Hardware Platform
Requirement Motivation:
The system shall search a 50,000 ft2 indoor environment.
The system shall maintain flight for at least 10 minutes.
The system shall carry an additional payload to be delivered.
Proposed Solution (1st iteration) :
Aliencopter Bee Quadcopter
Guidance sensor suite

## Slide 15
AlienBee Power and Mass Budgets
Item | QTY | Mass [g] | Curr [mA] | [mW]
Turnigy Nano-Tech LiPo Battery | 1 | 482.7 | -- | --
Odroid XU4 | 1 | 64.2 | 800 | 4000
3DR Radio | 1 | 26.2 | 100 | 330
Pixhawk | 1 | 40.3 | 175 | 1500
FLIR Lepton LWIR Camera | 1 | 0.55 | 5 | 150
Customer Payload (1lb) | 1 | 453.59 | -- | --
AlienBee Quad (Motor, Structure) | 1 | 43 | -- | --
DJI 9443 Propellor (E300) | 4 | 19 | -- | --
Guidance | 1 | 291 | 540 | 12000
ASUS Xtion Pro Live – RGBD camera | 1 | 115 | 500 | 2500
LIDAR-Lite v2 | 1 | 28.1 | 100 | 550
Windows Lifecam Studio Camera | 1 | 128 | 500 | 2500
TOTAL - Guidance |  | 2380 | 1670 | 17980
TOTAL - RGBD |  | 2360 | 2230 | 11530

## Slide 16
AlienBee Endurance vs. Payload

## Slide 17
FlyNet: Autonomous Quadcopter Search and Rescue
System | Mass Normal (1lb PL) [kg] | Endurance [min] | Endurance w/ 1lb PL [min]
AlienBee w/ RGBD | 1.91 (2.36) | 11.3 | 8.4
AlienBee w/ Guidance | 1.93 (2.38) | 11.4 | 8.5

## Slide 18
AlienBee Copter with Custom Modifications
Custom Plastic
Landing Gear
Custom blade guards created from a Hula Hoop

## Slide 19
Autonomous Quadcopter Control
Requirement Motivation:
The system shall perform a search for targets in unknown environments with limited prior information.
The system shall be completely autonomous after mission initialization.
Proposed Solution (1st iteration) :
Onboard single board computer (SCB) to perform planning and navigation calculations.
Interface with Pixhawk autopilot and use onboard controllers for position/velocity control
Trajectory planning and obstacle avoidance will be done on the onboard companion computer, position and velocity setpoints sent to autopilot
If onboard controllers are sufficient, modifications will be made to onboard controls architecture

## Slide 20
Pixhawk Functionality

## Slide 21
Onboard Computer – Pixhawk Interface

## Slide 22
Pixhawk Control Architecture

## Slide 23
Localization and Mapping
Requirement Motivation:
The system shall perform a search for targets in unknown environments with limited prior information.
Vehicles shall maintain a map of obstacles.
Vehicles shall communicate maps with other autonomous agents and with human responders (post mission).
Proposed Solution (1st iteration) :
Guidance sensor suite by DJI
  Visual odometry with IMU Fusion
  Obstacle detection
RTAB Map ROS Package
  Mapping and localization refinement.
  Produces a metrically accurate 3-D map of the world while estimating observation location and motion in that map.

## Slide 24
Perception Sensor Suite
Inertial 6DOF inertial data is available with calibration parameters
Depth Dense metric depth imagery is available with a pinhole camera model
Visual Imagery is available with a pinhole camera model

## Slide 25
Perception Architecture

## Slide 26
Alternative SLAM Options
LSD-SLAM: Large Scale Dense SLAM: Requires scale parameter estimation external to the system to produce a metric map
RGBD-SLAM: Does not provide for loop closure detection (worse map quality in larger spaces)
Notes: Add actual map quality metrics here.

## Slide 27
Autonomous Target Identification
Requirement Motivation:
The system shall identify targets within 5 meters of a vehicle
The system shall track visually identified targets.
Proposed Solution (1st iteration) :
FLiR Long wave infrared camera for identification of humans
OpenCV packages for Target ID
Custom Multiple Hypothesis tracker for tracking multiple targets in frame
Integration with sensor pose and motion estimates

## Slide 28
Tracking Method
Must process images at >= 5 Hz
Use C++ and OpenCV for low-overhead image processing
OpenCV has significant documentation and many useful libraries
OpenCV used in conjunction with Multiple Hypothesis Tracking (MHT) and Kalman Filtering will provide quick and accurate tracking solutions
Preliminary Sensor: Lepton 80x60 Pixel LWIR camera
  Provides contrast between human and background

## Slide 29
Tracking Architecture
Fused Sensor Velocity and Attitude Data
Object Level Tracker (Localizer)
FLiR Camera Image Data
(80x60 pixel map)
Track Identifier
Vehicle Map Position
(Local NED)
Time-synced Depth Image
Depth to FLiR Transformation (Calibration)
Perception Subsystem
Tracking Subystem
Groundstation

## Slide 30
Planning and Guidance
Requirement Motivation:
The vehicle shall avoid unrecoverable collisions with obstacles.
The system shall plan vehicle trajectories through the environment.
The vehicle shall move through the environment along planned trajectories to within TBD RMS error of the planned trajectory.
The aerial vehicle shall maintain a minimum distance of TBD from obstacles.
Proposed Solution (1st iteration) :
Generate precomputed trajectories from prior map in 2D.
Use obstacle distances from Guidance to trigger replanning.
Use updated maps from SLAM in replanning.
Support multiple guidance modes based on regimes of operation
  Target localization
  Door entry
  Featureless hallways

## Slide 31
FlyNet: Planning
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space

## Slide 32
FlyNet: Planning
“Roadblock”
“Target”
“Complete Block”
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space
Update plan based on dynamic environment

## Slide 33
“Roadblock”
“Target”
“Complete Block”
Generate initial path to explore space
Plan path for feasible dynamics
Plan path to avoid obstacles
Efficiently search space
Update plan based on dynamic environment
FlyNet: Planning

## Slide 34
FlyNet: Planning
Path Planning Alternatives
Cell Decomposition
  Break the map down into a grid
  Determine valid connections in the grid space
  Easy/fast to compute
  Cannot capture complex vehicle dynamics
Potential Fields
  Generate potential fields for plan
  Attract to desired trajectory
  Repel from obstacles
  Easy/fast to compute
  Struggles with local minima (ie rooms)
Sampling based methods
  Sample potential robot states randomly
  Connect states by checking for collisions and dynamics feasibility
  Captures high-dimensional robot states
  Captures complex problem constraints
See: http://ompl.kavrakilab.org/OMPL_Primer.pdf

## Slide 35
FlyNet: Planning
From: http://ompl.kavrakilab.org/OMPL_Primer.pdf
Path Planning Alternatives
Tree-Based Planners
  Seed a tree at the origin
  Randomly sample states near the current location
  Connect to all valid states based on collision detection and dynamics
  Grow this tree until we get to the goal
  Generates a single path from start to goal
  Need to grow a new tree for re-planning

## Slide 36
FlyNet: Planning
The Open Motion Planning Library
Open-source library with implementations of sample-based planning algorithms
Provides plug-ins to ROS or standalone c++
Supports basic modeling of quad rotors moving in 3D Environment
  Uses point-mass model of quad with thrust and angular acceleration as controls
  Environment is defined by CAD model
Initial path planning conducted for built-in environment using RRT
Goal
Start
Trajectory
Top-Down View

## Slide 37
FlyNet: Planning
The Open Motion Planning Library
Supports benchmarking of planners
So far, 3D planners seem to take significant amounts of time:
40 seconds for an empty space!

## Slide 38
FlyNet: Planning
Path Planning Issues
Path planning can generate a near optimal trajectory for getting between a start position and goal
Ability to plan with well known map can generate trajectories free of obstacles in highly complex environment
  Require minimal human input
3D path planning can be time consuming

## Slide 39
FlyNet: Planning
Path Planning Issues
Path planning can generate a near optimal trajectory for getting between a start position and goal <- We need to make the goals
Ability to plan with well known map can generate trajectories free of obstacles in highly complex environment <- Our environments contain uncertainties
  Require minimal human input
3D path planning can be time consuming <- We will likely need to re-plan frequently

## Slide 40
FlyNet: Planning
Block Diagram (In Development)
Offline Planner
POS Set-Point: NED
Attitude Set-Point: Ɵɸɣ
A-priori MAP (CAD)
Trajectory Memory
Re-Plan
Updated Map from SLAM
<
Obstacle Distance from Guidance
Target Localization
Command Mux
Target location estimate:
Local NED
Local NED from SLAM
Feature Detection
Feature Mode
Mode Select

## Slide 41
FlyNet: Planning
Path Forward
Determine method for generating goal points
  Base this on search coverage by projecting FLiR FoV
Explore options for 2D planning
  Faster re-planning
Improve quadrotor model in OMPL
  Give roll/pitch limits
  Potentially eliminate orientation as a state for exploration
Benchmark various planning options in OMPL
Generate 3D or 2D model of our test space

## Slide 42
FlyNet: End of Semester Test
Setup:
Known blueprint of area
Set up in Fleming Vicon Cage
Multiple rooms
Includes various hallway types
  Dead end
  Left turn
  Right turn

## Slide 43
FlyNet: End of Semester Test
“Roadblock”
“Target”
“Complete Block”
Unknowns:
Three Roadblocks placed into map
  4’ x 3’ wall
  Placed into map
Target placed into map
One Complete Block placed into map
  4’ x 6’ wall
  Height of standard wall for test environment

## Slide 44
FlyNet: End of Semester Test
Tasks to Complete:
Explore entire map
Avoid all obstacles
  Walls
  “Roadblocks”
  “Complete Blocks”
Return back to Entry Point with entire area mapped
“Roadblock”
“Target”
Entry/Exit Point
“Complete Block”

## Slide 45
First Semester Deliverables
One platform explores the Fleming lab space (2 rooms in addition to the main space) from a fixed starting point
One room has a static, tagged person.
One room has a static, unknown person.
Both are identified and the positions are reported to a ground station.
The quad will return to the starting position.

## Slide 46
Unaddressed Requirements
Target tagging
  QR Codes
  Processed through grayscale images
  Planned to address next semester
Multi Robots
  Will evaluate single flying robot this semester
  Budget provides overhead for at least 2 more based on current design
  Exploring ground robots using borrowed Tutlebots
  Examining architecture benefits
Multi Coordination
  Hooks built into planning
  Need to explore offline planning algorithms
  Need to explore efficient exploration algorithms
  Planned to address next semester

## Slide 47
Updated Requirements
Removed lighting requirements
  Guidance only provides reliable performance in good lighting conditions
  Benefits of Guidance to remaining requirements found to outweigh cost of removing lighting requirement
½ lb payload was found to give reasonable external payload budget while maintaining flight endurance requirements
Target ID rate requirement was reduced to 5Hz from 10Hz after reviewing available FLiR specs
  Only the export control variant was available
  This variant has a reduced frame rate

## Slide 48
Budget
Currently Spent:
  $1855.00 / 12.4%
Previous spending:
  Quadrotor platform
  Several single board computers (ODROID XU3)
Planned Spending:
  Secondary platform:
    Estimated to be $3000 per platform

## Slide 49
Schedule

## Slide 50
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 51
Obtaining Measurements from Images
Obtain Image
Mask Image
Find Contours
Save Features
Features:
Area
X Position
Y Position
Computed Features:
Δ Area
X Velocity
Y Velocity

## Slide 52
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 53
Generating Hypotheses
Objects of interest are detected at t0
t0

## Slide 54
Generating Hypotheses
New objects of interest are detected at t1 and they can be associated to form feasible tracks
t1

## Slide 55
Generating Hypotheses
New objects of interest are detected at t1 and they can be associated to form feasible tracks
t1

## Slide 56
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 57
Pruning Hypotheses
These may be down selected using a velocity constraint
t1

## Slide 58
Pruning Hypotheses
This velocity constraint is used as follows:
t1

## Slide 59
Pruning Hypotheses
Propagate the measurement’s state for one period:
t1

## Slide 60
Pruning Hypotheses
Apply an error bound:
t1

## Slide 61
Pruning Hypotheses
Prune hypotheses down to those that fit within velocity constraint
t1

## Slide 62
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 63
Prune Feasible Tracks
t2
Continue to form feasible tracks until tracks become improbable

## Slide 64
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 65
Prune Feasible Tracks
t3
Track is terminated after no new correlated objects

## Slide 66
A State Transition Matrix (STM) can be used to further constrain the location of future object measurements
State Transition Matrix

## Slide 67
Kalman Filtering

## Slide 68
Pruning Hypotheses
These may be down selected using a velocity constraint
t1

## Slide 69
Pruning Hypotheses
This velocity constraint is used as follows:
t1

## Slide 70
Pruning Hypotheses
Propagate the measurement’s state for one period:
t1
State Transition Matrix:

## Slide 71
Pruning Hypotheses
Apply an error bound:
t1

## Slide 72
Pruning Hypotheses
Prune hypotheses down to those that fit within velocity constraint
t1
Mahalanobis distance can be used to score possible matches:
Notes: ----- Meeting Notes (10/14/15 11:42) -----
Mahalanobis distance equation

## Slide 73
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 74
Prune Feasible Tracks
t2
Continue to form feasible tracks until tracks become improbable

## Slide 75
Algorithm Overview
Obtain Object Measurements
Generate Hypotheses
Prune Hypotheses
Correlate Hypotheses with Previous Feasible Tracks
Prune Feasible Tracks
Publish Confirmed Tracks

## Slide 76
Prune Feasible Tracks
t3
Track is terminated after no new correlated objects
Notes: ----- Meeting Notes (10/14/15 11:42) -----
Better colors

## Slide 77
A State Transition Matrix (STM) can be used to further constrain the location of future object measurements
State Transition Matrix
Notes: ----- Meeting Notes (10/14/15 11:42) -----
Put in state prop slide

## Slide 78
FlyNet: Autonomous Quadcopter Search and Rescue
Simulation
  Input  Flight controller  Airframe

## Slide 79
FlyNet: Autonomous Quadcopter Search and Rescue
Airframe Modelling
  Use Simulink 6DOF block to simulate equations of motion in the quadcopter body coordinate frame.

## Slide 80
FlyNet: Autonomous Quadcopter Search and Rescue
Applied Forces
  Gravity
  Motor thrust
  Aerodynamic forces
    Drag (lumped parameter model)
    Ground effects
Applied Moments
  Motor thrust
Other considerations
  Rotational dynamics
  Motor dynamics

## Slide 81
FlyNet: Autonomous Quadcopter Search and Rescue
Applied forces and moments

## Slide 82
FlyNet: Autonomous Quadcopter Search and Rescue
Flight control (actuator outputs for given roll, pitch, yaw, and throttle commands

## Slide 83
FlyNet: Autonomous Quadcopter Search and Rescue
Stabilize Mode

## Slide 84
FlyNet: Autonomous Quadcopter Search and Rescue
Altitude Control

## Slide 85
FlyNet: Autonomous Quadcopter Search and Rescue
Velocity Control

## Slide 86
FlyNet: Autonomous Quadcopter Search and Rescue
Position Control

## Slide 87
FlyNet: Autonomous Quadcopter Search and Rescue
Next steps
  Test hardware to determine accurate coefficients
    Motor thrust per (rotational velocity)2
    Motor rotational velocity per PWM input
    Quadcopter frame arm length
    Quadcopter moment of inertia
  Simulate Pixhawk controller in Simulilnk
  Validate simulation against experimental flight data

## Slide 88
Motor Current Draw
Thrust per motor:
For Hover: Thrust = Weight
Relating Power
r
I,V
η