## Slide 1
Path Planning – Driving Requirements
Level 1 | Level 2 | Level 3 | 
The system shall perform a search for targets. | The system shall navigate an unknown environment, using partial, prior information, e.g. building plans. | 1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles
 |  | 1.2.2 | The system shall plan vehicle trajectories through the environment
 |  | 1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present.
 |  | 1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles.
Level 1 | Level 2 | Level 3 | 
The system shall be autonomous, i.e. no human input once the system begins a search. | The system shall not have external navigation and targeting commands | 4.4.1 | The system shall make all navigation decisions onboard.

## Slide 2: 2 Steps
Path Planning – High Level
Step 1:
Waypoint Generation
  Develop list of nodes within operating space
  Exclude obstacles from list
Step 2:
Path determination
  Select nodes which:
    Lead from start -> goal
    Inherently avoid obstacles due to step 1

## Slide 3
Path Planning – Proposed Solution
Probabilistic Roadmap (PRM)
  Creates roadmap based on randomly sampled quadcopter configurations in open space.
Nearest Neighbor (NN) with 2-Opt
  NN: Traverses roadmap goals by minimizing the total distance traveled from one node to the next.
  2-Opt: Optimizes path takes a route that crosses over itself and reorders it so it does not.

## Slide 4
Path Planning – Methodology (PRM)
Probabilistic Roadmap (PRM)
Inputs
Map grid with obstacles marked
Desired number of nodes
Desired maximum neighbor node distance
Process
Samples possible collision-free quadcopter configurations at random
Connect all nodes within the configured maximum neighbor distance
Discard any routes that intersect with obstacles
Outputs
Roadmap containing collision free nodes and edges representing possible vehicle configurations
Coverage across entirety of open space possible if number of nodes is sufficiently high

## Slide 5
Path Planning – Methodology (PRM)
Probabilistically complete
  Chance to find route increases as number of nodes increases
Flexible and robust
  Collision avoidance threshold distance is configurable
  Number of sample nodes is configurable
  Maximum node neighbor distance configurable
  Re-plan only depends on updated map grid
Certain geometries where straight line connections cannot be made are difficult to navigate

## Slide 6
Path Planning – PRM Performance
Note: Performance based on Matlab computations
Processing time increases quadratically as the number of sampled configurations (nodes) increases
Increasing the number of nodes has diminishing returns for space coverage

## Slide 7
Path Planning – Methodology (NN+2Opt)
Nearest Neighbor + 2-Opt
Inputs
Auto-generated goal coordinates (a set of uniformly distributed points in free space)
PRM
Process
Build cost-weighted adjacency matrix for each goal coordinate
Compute path to the nearest goal for each goal
Optimize path using 2-Opt which removes unnecessary path crossover
Outputs
Position set points that efficiently traverse all goal coordinates.
Image courtesy of https://en.wikipedia.org/wiki/2-opt
2-Opt Example
Nearest Neighbors

## Slide 8
Path Planning – Methodology (NN+2Opt)
Able to handle multiple goals
  The computational effort increases as the number of goals (i.e. rooms) increases
Total area coverage is configurable
  Depends on the granularity of auto-generated goal points
  Goal points can be recalculated during the mission

## Slide 9
Path Planning – NN+2Opt Performance
Note: Performance based on Matlab computations
Chart: Processing Time vs Number of Goals
| 1 | 4 | 7 | 6 | 6 | 10 | 14 | 14 | 14 | 10 | 6 | 7 | 1 | 4 | 4
Y-Values | 0.166 | 0.4434 | 1.1373 | 0.7026 | 0.6062 | 3.2837 | 5.9043 | 5.746 | 6.1816 | 3.125 | 0.48767 | 1.1477 | 0.010258 | 0.15137 | 0.33065
Processing time increases quadratically as the number of goals increases
Goals are auto-generated for uniform coverage of the open space

## Slide 10
Path Planning – Proposed Solution
Voronoi path generation
  Generates nodes which are equidistant from obstacles
A* search
  Least cost node selection
  Cost = g(n) + h(n)
    g(n) = known cost (previously traversed)
    h(n) = estimate of node -> goal distance

## Slide 11
Path Planning - Methodology
Voronoi Node Generation
Inputs
Array of X and Y values that represent obstacles
Process
Outputs
Ordered list of polygon vertices representing points equidistant from obstacles

## Slide 12
Path Planning – Methodology (Voronoi)
Fewer nodes to evaluate than probabilistic methods
Optimum obstacle margin
  Paths automatically as far from obstacles as possible
Open spaces are often node sparse
  Depending on size of room, could require node addition to fill out space

## Slide 13
Path Planning – Voronoi Performance
Processing time is more or less linear
Note that our space is define in 340 (red *)

## Slide 14
Path Planning - Methodology
A*
Inputs
Array of X and Y values that represent waypoint possibilities
Process
Determine path based on least cost approach
Cost = g(n) + h(n)
  g(n) = known cost (previously traversed)
  h(n) = estimate of node -> goal distance
Outputs
Array of nodes defining path

## Slide 15
Path Planning – Summary
Level 3 |  | PRM/NN+2Opt Solution
1.2.1 | The vehicles shall avoid unrecoverable collisions with obstacles | - Nodes are randomly placed in open space. - Collision-prone node connections are discarded.
1.2.2 | The system shall plan vehicle trajectories through the environment | - Roadmap provides collision-free paths to most points in open space. - NN+2Opt method provides a trajectory to visit most of the open space on the roadmap.
1.2.3 | The vehicles shall move through the environment along planned trajectories to within 20 RMS error of the planned trajectory when no obstacles are present. | - NN+2Opt provides a trajectory plan that avoids obstacles and visits most of the open space on the roadmap.
1.2.4 | The aerial vehicle will maintain a minimum distance of 5 cm from obstacles | - PRM has the capability to configure the minimum distance from obstacles.
4.4.1 | The system shall make all navigation decisions onboard. | - PRM approach provides position set points in open space with collision-free paths between them.

## Slide 16
Path Planning – Backup Slides
Notes: Incomplete Matlab algorithmic demonstration

## Slide 17
FlyNet: Autonomous Quadcopter Search and Rescue